## Slide 1
EXOSKELETON LABORATORY
ICNR 2026
Data-Driven Compensation of Human–Robot Misalignment for Human Hip Kinematics Estimation in Wearable Robots
Chanyoung Ko and Kyoungchul Kong*
Exoskeleton Laboratory, Department of Mechanical Engineering, KAIST, Daejeon, Republic of Korea · kkyle0927@kaist.ac.kr; kckong@kaist.ac.kr (*corresponding author)
The wearer's own thigh angle, read from the robot's own sensors. No body-worn sensors, no motion capture.
Background
• Robot-mounted sensors measure the robot, not the wearer's anatomical thigh angle.
• Trunk rotation skews the trunk-fixed robot frame off the anatomical hip axis.
• Body-worn IMUs would fix this, at a usability and form-factor cost.
• The raw robot angle is off by 6.72° on average, worse when assistance is on.
Robot System
• Bilateral hip exoskeleton (Angel KIT H10), 10 N·m per side
• Onboard sensing: hip encoders, trunk IMU, pelvis-side robot-frame IMU
• θrobot = θencoder − θIMU − θcalibration, from a T-pose standing calibration after donning
• τpeak = 4 / 7 N·m (lv4 / lv7), Tp = 0.1 s
• Embedded module: NVIDIA Jetson Orin NX
• Everything the estimator needs is already mounted on the robot.
Methodology
Biomechanical cue
Trunk and pelvis counter-rotate during gait, and the robot frame rides on the trunk, so trunk yaw carries information about the discrepancy that the robot's own IMU already measures.
Relative yaw grows with walking speed and is negatively correlated with the discrepancy in all ten participants analysed.
Estimator
θrobot (left hip)
θrobot (right hip)
θ̃yaw trunk-IMU yaw (0.1 Hz high-pass)
Calibration: one 1.0-s standing window after donning. No motion-capture label is used at any point during inference.
8,658 parameters · fully causal · no actuator current · no body-worn sensor
A biomechanically motivated input, compact enough for the robot's own embedded computer.
Experiment
• 16 healthy adults · 11.7 h of robot–mocap data at 100 Hz
• 0.75 / 1.00 / 1.25 m/s and stop-and-go; assist lv0 / lv4 / lv7
• Reference: 12-camera Vicon, three thigh markers, T-pose zeroed
• Leave-one-subject-out over participants
• Motion capture trains and scores the estimate; never used at inference.
Results
• Accuracy on unseen participants
• 16-fold leave-one-subject-out: −3.15° vs the raw robot angle (95% CI −3.79 to −2.47°, p < 0.001), lower in all 16 held-out participants.
• −0.28° vs the no-yaw network (p = 0.039); −0.70° vs linear Ridge (p = 0.002).
• Conditions the model never saw
• Each target condition (assistance, faster walking, stop-and-go) was excluded from training, validation and model selection.
• Overall MAE fell 35–53% relative to the raw robot angle across all three shifts.
• Where the raw angle fails most
• High-flexion MAE: 14.23° → 4.21° (−70.4%) under assistance.
• Raw error grows with assistance level (7.67° → 8.94°); Proposed stays flat (3.74° → 4.09°).
• What this makes possible
• Raw overstates the lv0→lv7 ROM change by 172%, Proposed only 50%; samples above 5° error fall from 58.4% to 30.1%.
• 2.642 ms mean latency and 8,658 parameters on a Jetson Orin NX may enable estimator-in-the-loop use; closed-loop control was not verified.
Evaluated in 16 healthy adult male participants, one hip exoskeleton and one low-magnitude assistance profile. · KAIST IRB 2025-295 · Supported by NRF Korea (MSIT) No. 2022R1A3B1077880